POLIQUIN MACHINERY INC.

32 Nineteenth Street● Auburn, ME 04210●Phone: (207)784-1999●Fax: (207)795-6198●www.poliquinmachinery.com

A Proud member the Machine Tool Industry for Over 30 Years

We are pleased to offer, subject to prior sale the following:

- Pre-owned Mori Seiki Vertical Machining Center

Model: MV-40E

Year of Manufacture: 2000

Location: New Hampshire

Condition: Very Good.  In Production.

# SPECIFICATIONS

220/60/3 10HP

Fanuc MSC-500

Table: 35” x 18”

Travels: X-22”, Y-16”, Z-18”

Spindle Nose to Table Top: 6” – 24”

Max Table Load: 660 Lbs.

Spindle Taper: BT 40

Spindle Speed: 8,000 RPM

20 Station ATC

Coolant

Price $25,500.00

To the best of our knowledge, the specifications contained herein are accurate but should be verified at time of inspection.  If you have any questions please call (207) 784-1999.

Sincerely,

Greg Poliquin