POLIQUIN MACHINERY INC.

32 Nineteenth Street● Auburn, ME 04210● (207)784-1999●Fax: (866)758-9208●greg@poliquinmachinery.com

A Proud member the Machine Tool Industry for Over 30 Years

We are pleased to offer, subject to prior sale the following:

(1) Pre-owned Hyundai WIA Horizontal Machining Center

Model: KH-63G

Year of Manufacture: 2012

Location: Massachusetts

Condition: Very Good Under Power Approximately 5500 Cutting Hours

# SPECIFICATIONS

220/3/60 30HP

Fanuc 31i-Model A CNC

Manual Pulse Generator

Shuttle Type Auto Pallet Changer

(2) Pallet Size: 25" x 25"

Max Table Load: 2,200 Lbs.

Pallet Rotation: .001°

X-Axis Travel: 37.4"

Y-Axis Travel: 32.5"

Z-Axis Travel: 30"

Rapid Traverse: 790 IPM

Cutting Feed: 200 IPM

Spindle Speed: 8,000 RPM

Spindle Taper: Cat 50

ATC Capacity: 90 Station

Coolant Through Spindle

Chip Conveyor

Machine Weight: 30,500 Lbs.

Floor Space: (LxWxH) 127” x 190” x 123”

Price: POR

To the best of our knowledge, the specifications contained herein are accurate but should be verified at time of inspection.  If you have any further questions please call me at (207) 784-1999.

Sincerely,

Greg Poliquin